## Slide 1
JADE, a robust and expandable platform for neutronics V&V
D. Laghi1*, A. Bittesnich1, A. Valentine2, S.C. Bradnam2, M. Fabbri1, M. Campos1, M. Di Giacomo1, A. Milocco1
OpenMC Application to Tokamak Neutronics Analysis Meeting 30/05/2025
(1) F4E, Josep Pla 2 B3, Barcelona 08019, Spain
(2) UKAEA, Culham Campus, Abingdon, OX14 3DB, United Kingdom

## Slide 2: Outline
JADE: Why, What, When
The JADE ecosystem
JADE v4 and OpenMC
How to implement a new benchmark, a practical example
Future plans and conclusions

## Slide 3
Why?, What?, When?

## Slide 4: WHY JADE development started
Nuclear data production is a complex procedure that require extensive Verification and Validation (V&V)

## Slide 5: WHAT is JADE
Great number of benchmark to be automatically generated and run
Run of MC transport codes
Vast amounts of outputs are produced
Meaningful automatic post-processing
“Brute Force” ideally scanning all reactions and isotopes
Computational benchmarks to assess impact of changes in “real-life” applications of interest
Experimental benchmarks to help with validation of XS and codes
VERIFICATION
VALIDATION
More XS/quantities tested
Higher physical relevance

## Slide 6: WHEN: Historical recap
10/2018
U. Fisher highlight the needs for more automated V&V in FENDL
10/2019
Work on JADE starts as D. Laghi Ph.D. project
01/2021
First JADE major release (v1.0.0)
11/2022
UKAEA joins the project to port JADE to linux and introduce code2code capabilities
02/2024
JADE applied with success to FENDL 3.2b V&V campaign (endorsement from IAEA NDS)
03/2024
v3.0.0 is released. Porting to linux is completed and limited OpenMC capabilities are introduced
11/2024
Creation of the JADE V&V ecosystem with v3.1.0
04/2025
JADE v4.0.0
05/2025
Restoring of all v3 benchmarks + bug corrections with v4.1.0

## Slide 7
The JADE ecosystem

## Slide 8: JADE V&V ecosystem
https://github.com/JADE-V-V
External dependencies
JADE V&V repos
https://github.com/IAEA-NDS/open-benchmarks

## Slide 9: JADE WebApp

## Slide 10: A few numbers
25
Unique benchmarks implemented
3
OpenMC
149
Different inputs
4
Papers featuring JADE
32
400+
11
Commits in the last 12 months
Citations
Unique contributors so far

## Slide 11
JADE v4 and OpenMC

## Slide 12: Main achievements of v4.0.0
Re-think JADE to be a code-lib 2 code-lib comparison. Not code2code or lib2lib.
Full implementation of OpenMC (for the available benchmark inputs)
Implement a structure that clearly isolates (by inheritance of specific abstract classes) the extra python code needed to support an additional transport code.
No additional programming for new benchmarks (including experimental). Everything is handled by ad hoc YAML configuration files.
Raw data (csv files) are now a stronger interface. They are the end point of transport code-dependent processing and the starting point of the JADE plotting and excel. This facilitates the integration with 3rd party post-processors like the WebApp.
Software design best practices were applied during refactoring.
The codebase (number of lines) has been reduced to only 1/3 with respect to v3.1.0 one.

## Slide 13: Tallies comparison -> Results comparisons
TALLY RESULT
For each tally a standard pandas DataFrame is produced (for all transport codes).
Column headers are tally binnings. Names are standardized.
MOD1
Tally MODIFIERS:
Scale
To lethargy
Add column
Replace values
…
MOD2
MODn
…
Simulation output parsing
MODIFIED TALLY
COMB
MODIFIED TALLY
COMB
MODIFIED TALLY
RESULT
Tally COMBINATORS:
No actions
Sum
Concatenate
…
END of transport code dependent processing

## Slide 14: High level structure of JADE Engine
GUI
USER
DEVELOPERS
CLUSTER
LOCAL
CMD
Environmental
variables
Run and PP
Benchmarks configuration files
pip install jadevv

## Slide 15
A practical example: TUD-W

## Slide 16: Brief description of the experiment
More details in A. Kolsek presentation later today

## Slide 17: Prepare inputs for the new benchmark
INPUTS
EXP ERSULTS

## Slide 18: The raw result configuration file
Energy | Value | Error
1.1100 | [#/cm2/s] | …
… | … | …
pos1
Tally 1
Tally 2
Energy | Value | Error
0.41 | [#/cm2/s] | …
… | … | …
pos2
…
…
RAW RESULTS CONFIG FILE
Energy | Value | Error
1.11 | [#/cm2/s/MeV] | …
… | … | …
TUD-W_pos1 Neutron flux.csv

## Slide 19: The excel configuration file
TUD-W_pos1 Neutron flux.csv
TUD-W_pos1 Photon flux.csv
TUD-W_pos2 Neutron flux.csv
…
Case | Result | Energy | Value | Error
TUD-W_pos1 | Neutron flux | 1.11 | [#/cm2/s/MeV] | …
… | … | … | … | …
A global DataFrame is generated by JADE, Case and Result columns are always added
EXCEL CONFIG FILE

## Slide 20: The atlas configuration file
Case | Result | Energy | Value | Error
TUD-W_pos1 | Neutron flux | 1.11 | [#/cm2/s/MeV] | …
… | … | … | … | …
ATLAS CONFIG FILE

## Slide 21: Future plans
CONSOLIDATION
Review from experts to point out improvements on plot quality/types but also on methodologies (e.g. more TOF derivation instead of direct energy binning) and input improvements.
Schedule a hackathon to address the major comments that will arise -> v4.2.0
EXPANSION OF FEATURES
Keep implementing new benchmarks.
Gradually implement all available benchmarks also in OpenMC.
Implementation of CHI SQUARE and other KPIs to quantify libraries and/or codes performances.

## Slide 22: Conclusions
JADE is an open-source, robust and expandable platform for nuclear data and transport codes V&V.
Starting with JADE v4, OpenMC is fully supported.
Adding a new benchmark to JADE has never been easier.
We believe JADE can be strategic for supporting the adoption of OpenMC in fusion production environments.
Collaboration is always welcome!

## Slide 23: Thanks for you attention